## Slide 2: Multiple View Geometry
Frank Dellaert

## Slide 3: Outline
Intro
Camera Review
Stereo triangulation
Geometry of 2 views
  Essential Matrix
  Fundamental Matrix
Estimating E/F from point-matches
Notes: Triangulation: take two images and get 3D structure
What if we
Structure from motion: Multiple cameras: more accurate

## Slide 4: Why Consider Multiple Views?
P
P'
x
X
x'
Answer: To extract 3D structure via triangulation.

## Slide 5: Stereo Rig
Top View
Convenient when searching for correspondences.
Matches on Scanlines

## Slide 6: Feature Matching !
Notes: Show two images
How can we match them up ?

## Slide 7: Real World Challenges
Good news: Geometry constrains possible correspondences.
  4 DOF between x and x'; only 3 DOF in X.
  Constraint is manifest in the Fundamental matrix
  F can be calculated either from camera matrices or a set of good correspondences.
Bad News: Good correspondences are hard to find

## Slide 8: Geometry of 2 views ?
What if we do not know R,t ?
Caveat:
  My exposition uses different R, t
  but more intuitive (IMHO)
  I use [RT|-RTt] = RT [I|-t] camera matrices
  Szeliski uses [R|t]
Notes: Very cool, but now, suppose we don’t know where images were taken from
Now what ?

## Slide 9: Epipolar Geometry
C’
C
P
p
p’
M’= RT[I|-t]
M=[I|0]
t
?
Where can p appear ?
Notes: Very handy to know something about geometry
For example, if I have 2 views, one point, where could it be in other view ?
Suppose for now we know the geometry…
Picture: two views, question mark

## Slide 10: Image of Camera Center
epipole
M’= RT[I|-t]
M=[I|0]
Notes: Let’s ask a simpler question: two views, where is image of other camera in view 1 ?
We call this the epipole

## Slide 11: Example: Cameras Point at Each Other
Epipolar Lines
Top View

## Slide 12: Epipoles
Epipoles inside the image: zoom-like setup.

## Slide 13: Epipoles
Epipoles in near-stereo config.

## Slide 14: Epipoles
Camera Center C’ in first view:
Origin C in second view:

## Slide 15: Image of Camera Ray ?
epipole
M’= RT[I|-t]
M=[I|0]
Notes: Now, slightly more thinking. What is image of a ray ?

## Slide 16: Point at infinity
Given p’, what is corresponding point at infinity [x 0] ?
Answer for any camera M’=[A|a]:
A-1 = Infinite homography
In our case M’=[RT|-RTt]:
Notes: How to calculate them ?

## Slide 17: Sidebar: Infinite Homographies
Homography between
  image plane
  plane at infinity
Navigation by the stars:
  Image of stars = function of rotation R only !
  Traveling on a sphere rotates viewer

## Slide 18: Epipolar Line Calculation
1) Point 1 = epipole e=t
2) Point 2 = point at infinity
3) Epipolar line = join of points 1 and 2
Notes: How to calculate them ?

## Slide 19: Epipolar Lines
C’
C
e=t
e’
P
p
p’
P
p=Rp’
M’= RT[I|-t]
M=[I|0]
Notes: Illustrate by stepping through

## Slide 20: Epipolar lines
e=t
p=Rp’
Notes: Now, slightly more thinking. What is image of a ray ?

## Slide 21: Epipolar Plane
C’
C
e=t
e’
P
p
p’
M’= RT[I|-t]
M=[I|0]
Notes: Other way to see it: Plane formed by C, C’, and P

## Slide 22: Essential Matrix
mapping from p’ to l
E = 3*3 matrix
Because p is on l, we have

## Slide 23: Essential Matrix E
C’
C
e=t
e’
P
p
p’
P
p=Rp’
M’= RT[I|-t]
M=[I|0]
R,t = 6 DOF
However, scale !
=> 5 DOF
Notes: Illustrate by stepping through

## Slide 24: Fundamental Matrix
FUNDAMENTAL

## Slide 25: Uncalibrated Case
P
p=A-1p’
M’=K’[RT|-RTt]
M=K[I|0]
M’=K-1K’[RT|-RTt]
M=[I|0]
M’= [A|a]
M=[I|0]
C’
C
e=-A-1a
e’=a
P
p
p’
Notes: Illustrate by stepping through

## Slide 26
Uncalibrated Case, Forsyth & Ponce Version
Fundamental Matrix
(Faugeras and Luong, 1992)

## Slide 27: Fundamental Matrix
mapping from p’ to l
F = 3*3 matrix
Because p is on l, we have

## Slide 28: Fundamental Matrix F
C’
C
e=t
e’
P
p
p’
P
p=A-1p’
M’= [A|a]
M=[I|0]
3x3 = 9 DOF
However, scale, rank 2 !
=> 7 DOF
Notes: Illustrate by stepping through

## Slide 29
Properties of the Fundamental Matrix
Fp’ is the epipolar line associated with p’.
FTp is the epipolar line associated with p.
FTe=0 and Fe’=0.
F is singular.

## Slide 30
Non-Linear Least-Squares Approach
(Luong et al., 1993)
Minimize
with respect to the coefficients of F , using an
appropriate rank-2 parameterization.
d(p, l) = point to line distance = (ax + by + cw)/sqrt(a2 + b2)
d2 (p, l) = |ax + by + cw|2/(a2 + b2)

## Slide 31
The Eight-Point Algorithm (Longuet-Higgins, 1981)
|F | =1.
Minimize:
under the constraint
2

## Slide 32
The Normalized Eight-Point Algorithm (Hartley, 1995)
Center the image data at the origin, and scale it so the mean squared distance between the origin and the data points is 2 pixels:
qi = T pi qi’ = T’ pi’.
Use the eight-point algorithm to compute F from the points qi and q’i.
Enforce the rank-2 constraint.
Output T-1F T’.