## Slide 3: 3.1.1 Pixel transforms
Contrast
Brightness
Gamma
Histogram equalization
Arithmetic
Compositing

## Slide 4: Contrast
g(x) = a f(x), a=1.1

## Slide 5: Brightness
g(x) = f(x) + b, b=16

## Slide 6: Gamma correction
gamma = 1.2

## Slide 7: Histogram Equalization
Non-linear transform to make histogram flat
Still a per-pixel operation g(x) = h(f(x))

## Slide 8: Point-Process: Pixel/Point Arithmetic
120 | 122 | 140 | 142 | 143
121 | 80 | 40 | 144 | 10
122 | 81 | 40 | 0 | 151
125 | 80 | 40 | 0 | 152
126 | 70 | 40 | 0 | 153
120 | 122 | 140 | 142 | 143
121 | 120 | 141 | 144 | 147
122 | 121 | 144 | 146 | 11
125 | 121 | 144 | 145 | 10
126 | 121 | 145 | 147 | 13
120 | 122 | 140 | 142 | 143
121 | 120 | 141 | 144 | 147
122 | 121 | 144 | 146 | 11
125 | 121 | 144 | 145 | 10
126 | 121 | 145 | 147 | 13
120 | 122 | 140 | 142 | 143
121 | 80 | 40 | 144 | 10
122 | 81 | 40 | 0 | 151
125 | 80 | 40 | 0 | 152
126 | 70 | 40 | 0 | 153
+
240 | 244 | 280 | 284 | 286
121 | 200 | 181 | 288 | 157
122 | 202 | 184 | 146 | 162
125 | 201 | 184 | 145 | 164
126 | 191 | 185 | 147 | 166
=
-
0 | 0 | 0 | 0 | 0
0 | 40 | 101 | 0 | 137
0 | 40 | 104 | 146 | -140
0 | 40 | 104 | 145 | -142
0 | 191 | 185 | 147 | -140
=

## Slide 9: Pixel/Point Arithmetic: An Example
-
=
Image 1 - Image 2
Binary(Image 1 - Image 2)
Image 1
Image 2

## Slide 11: Image filtering
Image filtering: compute function of local neighborhood at each position
Really important!
  Enhance images
    Denoise, resize, increase contrast, etc.
  Extract information from images
    Texture, edges, distinctive points, etc.
  Detect patterns
    Template matching
  Deep Convolutional Networks

## Slide 12
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Example: box filter

## Slide 13
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 14
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 15
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 16
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 17
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 18
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 19
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 20
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 21
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 22
Smoothing with box filter

## Slide 23: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 24: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 25: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 26: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 27: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 28: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe

## Slide 29: Sharpening
Source: D. Lowe

## Slide 30: Other filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel

## Slide 31: Other filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel
Notes: Questions at this point?

## Slide 32: Filtering vs. Convolution
2d filtering
  h=filter2(f,I); or h=imfilter(I,f);
2d convolution
  h=conv2(f,I);
I=image
f=filter

## Slide 33: Key properties of linear filters
Linearity:
imfilter(I, f1 + f2) =
imfilter(I,f1) + imfilter(I,f2)
Shift invariance: same behavior regardless of pixel location
imfilter(I,shift(f)) = shift(imfilter(I,f))
Any linear, shift-invariant operator can be represented as a convolution
Source: S. Lazebnik
Notes: f is image

## Slide 34: More properties
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
  But particular filtering implementations might break this equality
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = [0, 0, 1, 0, 0], a * e = a
Source: S. Lazebnik

## Slide 35
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian
Notes: e^0 = 1, e^-1 = .37, e^-2 = .14, etc.

## Slide 36
Smoothing with Gaussian filter

## Slide 37
Smoothing with box filter

## Slide 38: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
  Images become more smooth
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width σ√2
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 39: Separability of the Gaussian filter
Source: D. Lowe

## Slide 40: Separability example
*
*
=
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:
Notes: Convolution vs filtering doesn’t matter here because the filter is symmetric

## Slide 41: Hybrid Images
A. Oliva, A. Torralba, P.G. Schyns, “Hybrid Images,” SIGGRAPH 2006

## Slide 42
Why do we get different, distance-dependent interpretations of hybrid images?
?
Slide: Hoiem

## Slide 45: Median filters
A Median Filter operates over a window by selecting the median intensity in the window.
What advantage does a median filter have over a mean filter?
Is a median filter a kind of convolution?
Slide by Steve Seitz
Notes: Better at salt’n’pepper noise
Not convolution: try a region with 1’s and a 2, and then 1’s and a 3

## Slide 46: Comparison: salt and pepper noise
Slide by Steve Seitz

## Slide 47: Bilateral filtering

## Slide 48: Morphological Operators

## Slide 50
Why does the Gaussian give a nice smooth image, but the square filter give edgy artifacts?
Gaussian
Box filter
Notes: Things we can’t understand without thinking in frequency

## Slide 51
Why does a lower resolution image still make sense to us? What do we lose?
Image: http://www.flickr.com/photos/igorms/136916757/
Slide: Hoiem

## Slide 52: Thinking in Frequency
Slides: Hoiem, Efros, and others

## Slide 53: Jean Baptiste Joseph Fourier (1768-1830)
had crazy idea (1807):
Any univariate function can be rewritten as a weighted sum of sines and cosines of different frequencies.
Don’t believe it?
  Neither did Lagrange, Laplace, Poisson and other big wigs
  Not translated into English until 1878!
But it’s (mostly) true!
  called Fourier Series
  there are some subtle restrictions
...the manner in which the author arrives at these equations is not exempt of difficulties and...his analysis to integrate them still leaves something to be desired on the score of generality and even rigour.
Laplace
Lagrange
Legendre

## Slide 54: Example: Music
We think of music in terms of frequencies at different magnitudes
Slide: Hoiem

## Slide 55: Frequency Spectra
example : g(t) = sin(2πf t) + (1/3)sin(2π(3f) t)
=
+
Slides: Efros

## Slide 56: Frequency Spectra

## Slide 57: Frequency Spectra
=
+
=

## Slide 58: Frequency Spectra
=
+
=

## Slide 59: Frequency Spectra
=
+
=

## Slide 60: Frequency Spectra
=
+
=

## Slide 61: Frequency Spectra
=
+
=

## Slide 62: Frequency Spectra
=

## Slide 63: Fourier analysis in images
Intensity Image
Fourier Image
http://sharp.bu.edu/~slehar/fourier/fourier.html#filtering

## Slide 64: Fourier Transform
Fourier transform stores the magnitude and phase at each frequency
  Magnitude encodes how much signal there is at a particular frequency
  Phase encodes spatial information (indirectly)
  For mathematical convenience, this is often notated in terms of real and complex numbers
Amplitude:
Phase:

## Slide 65: Fourier Transform Pairs

## Slide 66: Fourier Transforms of Filters

## Slide 67: Man-made Scene

## Slide 68: Can change spectrum, then reconstruct

## Slide 69: Low and High Pass filtering

## Slide 70: The Convolution Theorem
The Fourier transform of the convolution of two functions is the product of their Fourier transforms
Convolution in spatial domain is equivalent to multiplication in frequency domain!

## Slide 71: Filtering in spatial domain
-1
0
1
-2
0
2
-1
0
1
*
=

## Slide 72: Filtering in frequency domain
FFT
FFT
Inverse FFT
=
Slide: Hoiem

## Slide 73
Why does the Gaussian give a nice smooth image, but the square filter give edgy artifacts?
Gaussian
Box filter
Filtering
Notes: Things we can’t understand without thinking in frequency

## Slide 74
Gaussian

## Slide 75
Box Filter