## Slide 2: Feature-based Image Alignment
Geometric image registration
  2D or 3D transforms between them
  Special cases: pose estimation, calibration
Image credit Szeliski book

## Slide 3: 2D Alignment
3 photos
Translational model
Image credit Szeliski book

## Slide 4: 2D Alignment
Input:
  A set of matches {(xi, xi’)}
  A parametric model f(x; p)
Output:
  Best model p*
How?
Image credit Szeliski book

## Slide 5: 2D translation estimation
Input:
  Set of matches {(x1, x1’), (x2, x2’), (x3, x3’), (x4, x4’)}
  Parametric model: f(x; t) = x + t
  Parameters p == t, location of origin of A in B
Output:
  Best model p*
Image credit Szeliski book

## Slide 6: 2D translation estimation
Input:
  Set of matches {(x1, x1’), (x2, x2’), (x3, x3’), (x4, x4’)}
  Parametric model: f(x; t) = x + t
  Parameters p == t, location of origin of A in B
Question for class:
  What is your best guess for model p* ??
Image credit Szeliski book
Notes: What is your best guess? With one correspondence?
x1 = [600, 150], x1’ = [50, 50] -> x’ = x - t => t = x-x’ = [600-50, 150-50] = [550, 100]

## Slide 7: 2D translation estimation
How?
  One correspondence x1 = [600, 150], x1’ = [50, 50]
  Parametric model: x’ = f(x; t) = x + t
Image credit Szeliski book

## Slide 8: 2D translation estimation
How?
  One correspondence x1 = [600, 150], x1’ = [50, 50]
  Parametric model: x’ = f(x; t) = x + t => t = x’- x
=> t = [50-600, 40-150] = [-550, -100]
[-550, -100]
Image credit Szeliski book

## Slide 9: 2D translation via least-squares
How?
  A set of matches {(xi, xi’)}
  Parametric model: f(x; t) = x + t
  Minimize sum of squared residuals:
Image credit Szeliski book

## Slide 10: How to solve?
Jacobian
Hessian
Normal equations

## Slide 11: Linear models menagerie
All the simple 2D models are linear!
Exception: perspective transform
Figure credit Szeliski book

## Slide 12: 2D translation via least-squares
Image credit Szeliski book

## Slide 13: Oops I lied !!! Euclidean is not linear!
All the simple 2D models are linear!
Euclidean Jacobians are a function of θ!
Figure credit Szeliski book

## Slide 14: Nonlinear Least Squares

## Slide 15: Projective/H
Jacobians a bit harder
Parameterization:
x’= f(x,p):
And Jacobian:
Image credit Graphics Mill
(educational Use)

## Slide 16: Closed Form H
Taking x’=f(x,p):
Divide both sides by :
4 matches => system of 8 linear equations
Image credit Graphics Mill
(educational Use)

## Slide 17: RANSAC

## Slide 18: Motivation
Estimating motion models
Typically: points in two images
Candidates:
  Translation
  Homography
  Fundamental matrix

## Slide 19: Mosaicking: Homography
www.cs.cmu.edu/~dellaert/mosaicking

## Slide 20: Two-view geometry (next lecture)
Notes: Show two images
How can we match them up ?

## Slide 21: Omnidirectional example
Images by Branislav Micusik, Tomas Pajdla,
cmp.felk.cvut.cz/ demos/Fishepip/

## Slide 22: Simpler Example
Fitting a straight line

## Slide 23: Discard Outliers
No point with d>t
RANSAC:
  RANdom SAmple Consensus
  Fischler & Bolles 1981
  Copes with a large proportion of outliers
Image credit Choi et al BMVC 2009

## Slide 24: Main Idea
Select 2 points at random
Fit a line
“Support” = number of inliers
Line with most inliers wins
Image credit shutterstock, academic use

## Slide 25: Why will this work ?

## Slide 26: Best Line has most support
More support -> better fit
Image credit Wikipedia

## Slide 27: RANSAC
Objective:
  Robust fit of a model to data D
Algorithm
  Randomly select s points
  Instantiate a model
  Get consensus set Di
  If |Di|>T, terminate and return model
  Repeat for N trials, return model with max |Di|
Image credit Wikipedia

## Slide 28: In General
Fit a more general model
Sample = minimal subset
  Translation ?
  Homography ?
  Euclidean transorm ?

## Slide 29: Example
Euclidean: needs 2 correspondences (2*2>=3)
Here correct hypothesis has support of 4 (out of 5)
Including red into minimal sample (of 2) would likely yield low support

## Slide 30: How many samples ?
We want: at least one sample with all inliers
Can’t guarantee: probability P
E.g. P = 0.99
Image credit Wikipedia

## Slide 31: Calculate N
If = outlier probability =0.4
proportion of inliers p = 1- p=0.6
P(sample with all inliers) = ps s=2 -> ps=0.36
P(sample with an outlier) = 1-ps 0.64
P(N samples an outlier) = (1-ps)N N=3 -> 0.26
We want P(N samples an outlier) < 1-P (e.g. 0.01)
(1-ps)N < 1-P 0.64N < 0.01
N > log(1-P)/log(1-ps) N >10.3
Image credit Wikipedia

## Slide 32: Example
P=0.99
s=2
  = 5% => N=2
  = 50% => N=17
s=4
  = 5% => N=3
  = 50% => N=72
s=8
  = 5% => N=5
  = 50% => N=1177
Image credit Wikipedia

## Slide 33: Remarks
N = f(), not the number of points
N increases steeply with s
Image credit Wikipedia

## Slide 34: Distance Threshold
Requires noise distribution
Gaussian noise with 
Chi-squared distribution with DOF m
  95% cumulative:
  Line, F: m=1, t2=3.84 2
  Translation, homography: m=2, t2=5.99 2
I.e. -> 95% prob that d<t is inlier
Image credit Wikipedia

## Slide 35: Threshold T
Terminate if |Di|>T
Rule of thumb: T  #inliers
So, T = (1- )n = pn
Image credit Wikipedia

## Slide 36: Adaptive N
When is unknown ?
Start with = 50%, N=inf
Repeat:
  Sample s, fit model
  update as |outliers|/n
  set N=f(, s, p)
Terminate when N samples seen
Image credit Wikipedia

## Slide 37: Summary: RANSAC
Objective:
  Robust fit of a model to data D
Algorithm
  Randomly select s points
  Instantiate a model
  Get consensus set Di
  If |Di|>T, terminate and return model
  Repeat for N trials, return model with max |Di|
Image credit Wikipedia

## Slide 38: Pose Estimation in VR
https://youtu.be/nrj3JE-NHMw

## Slide 39: Review: 2D Alignment
Input:
  A set of matches {(xi, xi’)}
  A parametric model f(x; p)
Output:
  Best model p*
How?
Image credit Szeliski book

## Slide 40: Now: 3D-2D Alignment
Input:
  A set of 3D->2D matches {(Xi, xi)}
  A parametric model f(X; p)
Output:
  Best model p*
How?
Image credit Szeliski book

## Slide 41: Pose Estimation
Input:
  A set of 2D measurements xi of known 3D points Xi
  Parametric model is camera matrix P, i.e., x = f(X; P)
Output:
  Best camera matrix P
How?
Image credit Szeliski book

## Slide 42: Review: Projective Camera Matrix
Chapter 2 in book
Homogeneous coord.
3D TO 2D projection: x = K[R|t]X = PX where P = 3x4 camera matrix and K the 3x3 calibration

## Slide 43: Camera Extrinsics: a Pose in 3D
What is the geometric meaning of R and t ??
Intuitive: camera is at a position wtc Indices say: camera in world coordinate frame
wtc

## Slide 44: Camera Extrinsics: a Pose in 3D
What is the geometric meaning of R and t ??
Rotation is given by 3x3 matrix wRc whose columns are the camera axes wxc, wyc, wzc
wxc
wyc
wzc

## Slide 45: Camera Extrinsics: a Pose in 3D
What is the geometric meaning of R and t ??
Transforming point Xi from world to camera coordinates: wXi – wtc = wRc cXi
wXi
wXi - wtc

## Slide 46: Camera Extrinsics: a Pose in 3D
Expressed in homogeneous coordinates:
cXi = wRcT (wXi - wtc) = wRcT [I| - wtc] wXi = [wRcT | - wRcT wtc] wXi = [cRw | ctw] wXi = [R|t] wXi
wXi
cXi

## Slide 47: Camera Extrinsics: a Pose in 3D
Conclusion: when people write cXi = [R|t] wXi they are talking about (unintuitive) [cRw | ctw]
We like use (intuitive) cXi = wRcT [I| - wtc] wXi
wXi
cXi

## Slide 48: Revision: Projective Camera Matrix
Homogeneous coord.
3D TO 2D projection: Camera-centric: x = K[cRw | ctw] X = PX World-centric: x = K wRcT [I | - wtc] X = PX P = same 3x4 camera matrix and K the 3x3 calibration

## Slide 49: Looking at the (opaque) camera matrix
Can you interpret the columns of P with entities in the scene?
Answer:
P1 == the image of [1 0 0 0]
P2 == the image of [0 1 0 0]
P3 == the image of [0 0 1 0]
P4 == the image of [0 0 0 1]
What are those ?
[0 0 0 1] is easy…
Answer:
[0 0 0 1] is the origin, so P4 is the image of the origin.
[1 0 0 0] is a point at infinity in the X-direction, so it is the vanishing point of all lines parallel with the X direction!

## Slide 50: Vanishing points, revisited
Columns of P !
P4 is arbitrary: wherever you defined the world origin.
3
1
2
2
1
3
https://www.artinstructionblog.com/perspective-drawing-tutorial-for-artists-part-2

## Slide 51: Back to Pose Estimation!
Simple algorithm: just measure the coordinates of the origin and the three vanishing points?
Does not work :
  Columns are only measured up to a scale.
  4 points * 2DOF = only 8 DOF! Missing 11-8=3
  3 missing numbers are exactly those scales.

## Slide 52: Least Squares Pose Estimation…
Input:
  A set of 2D measurements xi of known 3D points Xi
  Parametric model is camera matrix P, i.e., x = f(X; P)
Output:
  Best camera matrix P

## Slide 53: Pose estimation = “Resectioning”
Opposite of triangulation.

## Slide 54: Pose estimation
In project 4, you will use scipy.optimize.least_squares to do exactly that. Working knowledge of 3D poses will be required.
Note before we compute the 2D reprojection error we need to convert back PX to non-homogeneous coordinates:
https://docs.scipy.org/doc/scipy/reference/generated/scipy.optimize.least_squares.html